## Slide 1
Air infiltration

## Slide 2
Heat Loss Calculation Review
HL=(Surface Area) (U-Factor) (rT)
U-Factor = 1 / RValue-Overall
  RValue
    Individual materials resistance level to heat flow
rT = Change in temperature
Notes: http://www.grc.nasa.gov/WWW/k-12/WindTunnel/Activities/Pascals_principle.html

## Slide 3
http://www.energystar.gov/ia/home_improvement/images/house-leaks-with-text-780.jpg
Air Infiltration
As structure gaps increase, air infiltration increases and heat loss increases

## Slide 4
Air Infiltration Calculation
Q = Lx P((A)(rT) + (B)(V2))
Q = Airflow in ft3/min
Lx = Leakage Area
A = Stack Coefficient = .0156
B = Wind Coefficient = .0119
V = Wind Velocity = x
  Madison Average is 9.0 mph

## Slide 5
Leakage Area = Lx
To solve for Lx we need to know what the Lateral Leakage (LL) is
  Lateral Leakage areas are exposed joints in a structure
LL = (Exposure)(Area)+…+ (Exposure)(Area)
Lx = (LL)(.07in2)
  .07in2 = Constant LL for every 1 lnft2
    lnft = Linear Foot

## Slide 6
Air Infiltration & Heat Loss
Due to the infiltration of air, heat will be lost
  As structure gaps increase, air infiltration increases, and heat loss increases
We need to calculate how air infiltration impacts heat loss
http://www.energystar.gov/ia/home_improvement/images/house-leaks-with-text-780.jpg

## Slide 7
Air Infiltration & Heat Loss Calculation
(Lx/12) (C) (rT) = HA
C = HVAC Constant = 1.085
HA = Heat Loss due to Air Infiltration in BTU / hour

## Slide 8
Safety Factors and Airflow
Safety factor (S.F)
  Plan ahead
Average person needs Q = 0.28 ft3/min
  5Q = 1.4 ft3/min
Plan for a S.F. of 2
  Q = 2.8 ft3/min
http://blogs.abcnews.com/photos/uncategorized/2007/08/02/ap_bridge_weight_070802_mai.jpg

## Slide 9
Balloon Effect
If only one hole (that are not LL) exists, a balloon effect will occur
Solution = Have more than one hole to accommodate
http://www.studioe3.com/lessons/images/new3.gif

## Slide 10
Example
NOTE: This example is not an example about the Case Study, rather an example on how to use the calculations.
We have a Rectangular Prism structure with the following parameters:
  Length = 6’
  Width = 4’
  Height = 4’
http://www.newbedford.k12.ma.us/elementary/gomes/stjohn/Subjects/Math/Geo/rectangular%20prism.jpg

## Slide 11
Example
‘Find the exposed Surface Area of the structure
Total Surface Area =
2lw + 2hw + 2lh =
2(6)(4) + 2(2)(4) + 2(6)(4) =
112’
http://www.newbedford.k12.ma.us/elementary/gomes/stjohn/Subjects/Math/Geo/rectangular%20prism.jpg

## Slide 12
Example
Solve for LL & Lx
LL = (exp)(area)+…+ (exp)(area) =
(4)(6)+(4)(4)+(4)(4) =
(24) + (16) + (16) =
LA = (LL)(0.07) =
(56)(0.07) =
http://www.newbedford.k12.ma.us/elementary/gomes/stjohn/Subjects/Math/Geo/rectangular%20prism.jpg
56’
3.92 in2

## Slide 13
Example
Solve for Airflow needed
  5 people need 2.8ft3/min = Q
  Accommodate for Balloon Effect (2)
Q(2) = Lx P((A)(rT) + (B)(V2))
2.8(2) = LB P((.0156)(80) + (.0119)(9.02))
5.6 = LB P((1.248) + (0.964))
5.6 = LB P(2.212)
5.6 = LB (1.487)
5.6/1.487 = LB
3.766 = LB

## Slide 14
Example
Is LB < LA ?
If Yes
  Proceed to Air Infiltration & Heat Loss Calculations
If No
  Add gaps to make LB < LA
  Redo LA to ensure LB < LA
  Repeat process until Yes
  Remember to subtract every gap added to the structure from the Surface Area

## Slide 15
Example
LB < LA is correct
Solve for Q to ensure suffocation does not occur
Q = LA P((A)(rT) + (B)(V2))
Q = 3.92 P((.0156)(80) + (.0119)(92))
Q = 5.622 ft3/min
Is Q/2 > 2.4 ft3/min?
  5.622 / 2 = 2.811 ft3/min
  Reconfirms that there is enough Airflow for breathing with a safety factor of 2

## Slide 16
Example
Find Heat Loss due to Air Infiltration
(LA/12) (C) (rT) = HA
(3.92/12)(1.085)(80) = HA
28.355 BTU/ Hour = HA
Remember:
  1 average person gives off 368.604 BTU/Hour of heat
  5 average people give off 1843.020 BTU/Hour of heat

## Slide 17
Example
Figure out what overall RValue is needed to maintain heat inside shelter at 60oF
HL – HA = (Surface Area)(U-Factor)(rT)
1843.020 – 28.355 = (112)(U)(80)
1814.665 = (8960)(U)
1814.665 / 8960 = U
0.203 = U
0.203 = 1/Rvalue
Rvalue = 1/0.203
4.926 = Rvalue of all materials needed on each wall section

## Slide 18
Example
Figure out the Wall Section materials and Rvalues of those materials to meet the U-Factor needed
FYI = 1/8” Corrugated Cardboard has an Rvalue of 0.184
http://digitalvintagelabels.com/images/LabelTrader_ABitofCardboard1_600.jpg