## Slide 1
Short Circuit & protection Devices

## Slide 2
The load can be things like an LED light, a blender or any object that converts electrical energy into another form of energy.
Most circuits usually have a load and two terminals that are connected to a load

## Slide 3
A short circuit occurs when two or more bare wires or connections touch each other
This is an unintended path for the electricity and can cause damage to the device, people or the environment it is placed in.

## Slide 4
Often bad or frayed insulation on wires is an indicator
of a potential short circuit.

## Slide 5
If a problem occurs in an electrical circuit, a fuse is used to break the connection and save the device or environment.
Blown Barrel Fuse

## Slide 6
In your house or apartment building, a fuse box or circuit breaker is used to protect the electrical circuits.
  Fuse boxes use cylindrical fuses that have to be replaced
  Circuit breakers “trip” when overloaded and have to be reset, not replaced.
Breaker Box
Fuse Box

## Slide 7
A GFCI outlet protects people from electrical shock, it is different from a fuse
  GFCI monitors the amount of current flowing from the hot (small slot) to neutral (large slot)
Even with a small mismatch in current, the GFCI trips the circuit at the outlet to protect.
Often these outlets are used outdoors, or near a sink
GFCI Outlet

## Slide 8
In your car there are multiple fuses in various places
  Fuse boxes can be in or under the dashboard
  Fuse boxes can be in the engine compartment
In-line fuses can also be used and are along the wire it protects
Fuse Box
In-line Fuse

## Slide 9
When replacing a fuse or breaker, only use the correct size for the circuit
  Undersized protection devices will trip quickly
  Oversized protection devices have the potential to cause damage to the device or environment
ALWAYS use the correct protection device, bypassing the fuse or using material other than the fuse can cause shock, damage to the device or the environment
Thermal image of an overheating circuit breaker
130.2ºf
54.4