## Slide 1
FMEA Failure Mode Effects Analysis

## Slide 2
AGENDA
Ice breaker
Opening
DFMEA
Break
DFMEA exercise
Lunch
PFMEA
Break
PFMEA Exercise
FMEA Jeopardy
Closing and Survey

## Slide 3
Quality and Reliability
Quality is a relative term often based on customer perception or the degree to which a product meets customer expectations
Manufacturers have long recognized that products can meet specifications and still fail to satisfy customer expectations due to:
  Errors in design
  Flaws induced by the manufacturing process
  Environment
  Product misuse
  Not understanding customer wants/needs

## Slide 4
Quality, Reliability and Failure Prevention
Traditionally quality activities have focused on detecting manufacturing and material defects that cause failures early in the life cycle
Today, activities focus on failures that occur beyond the infant mortality stage
Emphasis on Failure Prevention

## Slide 6
Failure Mode & Effects Analysis (FMEA)
FMEA is a systematic method of identifying and preventing system, product and process problems before they occur
FMEA is focused on preventing problems, enhancing safety, and increasing customer satisfaction
Ideally, FMEA’s are conducted in the product design or process development stages, although conducting an FMEA on existing products or processes may also yield benefits

## Slide 7
FMEA/FMECA History
The history of FMEA/FMECA goes back to the early 1950s and 1960s.
  U.S. Navy Bureau of Aeronautics, followed by the Bureau of Naval Weapons:
  National Aeronautics and Space Administration (NASA):
Department of Defense developed and revised the MIL-STD-1629A guidelines during the 1970s.

## Slide 8
FMEA/FMECA History (continued)
Ford Motor Company published instruction manuals in the 1980s and the automotive industry collectively developed standards in the 1990s.
Engineers in a variety of industries have adopted and adapted the tool over the years.

## Slide 9
Published Guidelines
J1739 from the SAE for the automotive industry.
AIAG FMEA-3 from the Automotive Industry Action Group for the automotive industry.
ARP5580 from the SAE for non-automotive applications.

## Slide 10
Other Guidelines
Other industry and company-specific guidelines exist. For example:
  EIA/JEP131 provides guidelines for the electronics industry, from the JEDEC/EIA.
  P-302-720 provides guidelines for NASA’s GSFC spacecraft and instruments.
  SEMATECH 92020963A-ENG for the semiconductor equipment industry.
  Etc…

## Slide 11
FMEA is a Tool
FMEA is a tool that allows you to:
  Prevent System, Product and Process problems before they occur
  reduce costs by identifying system, product and process improvements early in the development cycle
  Create more robust processes
  Prioritize actions that decrease risk of failure
  Evaluate the system, design and processes from a new vantage point

## Slide 12
A Systematic Process
FMEA provides a systematic process to:
  Identify and evaluate
    potential failure modes
    potential causes of the failure mode
  Identify and quantify the impact of potential failures
  Identify and prioritize actions to reduce or eliminate the potential failure
  Implement action plan based on assigned responsibilities and completion dates
  Document the associated activities

## Slide 13
Purpose/Benefit
cost effective tool for maximizing and documenting the collective knowledge, experience, and insights of the engineering and manufacturing community
format for communication across the disciplines
provides logical, sequential steps for specifying product and process areas of concern

## Slide 14
Benefits of FMEA
Contributes to improved designs for products and processes.
  Higher reliability
  Better quality
  Increased safety
  Enhanced customer satisfaction
Contributes to cost savings.
  Decreases development time and re-design costs
  Decreases warranty costs
  Decreases waste, non-value added operations
Contributes to continuous improvement

## Slide 15
Benefits
Cost benefits associated with FMEA are usually expected to come from the ability to identify failure modes earlier in the process, when they are less expensive to address.
  “rule of ten”
    If the issue costs $100 when it is discovered in the field, then…
    It may cost $10 if discovered during the final test…
    But it may cost $1 if discovered during an incoming inspection.
    Even better it may cost $0.10 if discovered during the design or process engineering phase.

## Slide 16
FMEA as Historical Record
Communicate the logic of the engineers and related design and process considerations
Are indispensable resources for new engineers and future design and process decisions.

## Slide 17
SFMEA, DFMEA, and PFMEA
When it is applied to interaction of parts it is called System Failure Mode and Effects Analysis (SFMEA)
Applied to a product it is called a Design Failure Mode and Effects Analysis (DFMEA)
Applied to a process it is called a Process Failure Mode and Effects Analysis (PFMEA).

## Slide 18
Design
Process
Components
Subsystems
Main Systems
Components
Subsystems
Main Systems
Machines
Tools,
Work Stations,
Production Lines,
Operator Training,
Processes,
Gauges
Focus:
Minimize failure
effects on the
System
Objectives/Goal:
Maximize System
Quality, reliability,
Cost and maintenance
Focus:
Minimize failure
effects on the
Design
Objectives/Goal:
Maximize Design
Quality, reliability,
Cost and maintenance
Focus:
Minimize failure
effects on the
Processes
Objectives/Goal:
Maximize
Total Process
Quality, reliability,
Cost and maintenance
Manpower
Machine
Method
Material
Measurement
Environment
system

## Slide 19
Why do FMEA’s?
Examine the system for failures.
Ensure the specs are clear and assure the product works correctly
ISO requirement-Quality Planning
  “ensuring the compatibility of the design, the production process, installation, servicing, inspection and test procedures, and the applicable documentation”

## Slide 20
What is the objective of FMEA?
Uncover problems with the product that will result in safety hazards, product malfunctions, or shortened product life,etc..
Ask ourselves “how the product will fail”?
How can we achieve our objective?
  Respectful communication
  Make the best of our time, it’s limited; Agree for ties to rank on side of caution as appropriate

## Slide 21
Potential Applications for FMEA
Component Proving Process
Outsourcing / Resourcing of product
Develop Suppliers to achieve Quality
Renaissance / Scorecard Targets
Major Process / Equipment / Technology
Changes
Cost Reductions
New Product / Design Analysis
Assist in analysis of a flat pareto chart

## Slide 22
What tools are available to meet our objective?
Benchmarking
customer warranty reports
design checklist or guidelines
field complaints
internal failure analysis
internal test standards
lessons learned
returned material reports
Expert knowledge

## Slide 23
What are possible outcomes?
Actual/potential failure modes
customer and legal design requirements
duty cycle requirements
product functions
key product characteristics
Product Verification and Validation

## Slide 24
How to Fmea…The Pre-Team Meeting
Prior to assembling the entire team, it may be useful to arrange a meeting between two or three key engineers
This could include persons responsible for design, quality, and testing.

## Slide 25
How to FMEA.. (cont.)
The purpose of this meeting is to:
  Determine scope
  Gather background reference material
  Create update block diagrams
  Identify team members
  Prepare an agenda, schedule, milestones
  Identify item functions, failure modes and their effects

## Slide 26
Block Diagram
The FMEA should begin with a block diagram for the system or subsystem
This diagram should indicate the functional relationship of the parts or components appropriate to the level of analysis being conducted.

## Slide 27
Assumptions of DFMEA
All systems/components are manufactured and assembled as specified by design
Failure could, but will not necessarily, occur

## Slide 28
Design FMEA Format
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Function

## Slide 29
General
Every FMEA should have an assumptions document attached (electronically if possible) or the first line of the FMEA should detail the assumptions and ratings used for the FMEA.
Product/part names and numbers must be detailed in the FMEA header
All team members must be listed in the FMEA header
Revision date, as appropriate, must be documented in the FMEA header
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 30
Function-What is the part supposed to do in view of customer requirements?
Describe what the system or component is designed to do
  Include information regarding the environment in which the system operates
    define temperature, pressure, and humidity ranges
List all functions
Remember to consider unintended functions
  position/locate, support/reinforce, seal in/out, lubricate, or retain, latch secure

## Slide 31
Function
EXAMPLE:
HVAC system must defog windows and heat or cool cabin to 70 degrees in all operating conditions (-40 degrees to 100 degrees)
- within 3 to 5 minutes
or
- As specified in functional spec #_______; rev. date_________
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 32
Potential Failure mode
Definition: the manner in which a system, subsystem, or component could potentially fail to meet design intent
Ask yourself- ”How could this design fail to meet each customer requirement?”
Remember to consider:
  absolute failure
  partial failure
  intermittent failure
  over function
  degraded function
  unintended function

## Slide 33
Failure Mode
EXAMPLES:
HVAC system does not heat vehicle or defog windows
HVAC system takes more than 5 minutes to heat vehicle
HVAC system does not heat cabin to 70 degrees in below zero temperatures
HVAC system cools cabin to 50 degrees
HVAC system activates rear window defogger
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 34
Consider Potential failure modes under:
Operating Conditions
  hot and cold
  wet and dry
  dusty and dirty
Usage
  Above average life cycle
  Harsh environment
  below average life cycle

## Slide 35
Consider Potential failure modes under:
Incorrect service operations
  Can the wrong part be substituted inadvertently?
  Can the part be serviced wrong? E.g. upside down, backwards, end to end
  Can the part be omitted?
  Is the part difficult to assemble?
Describe or record in physical or technical terms, not as symptoms noticeable by the customer.

## Slide 36
Potential Effect(s) of Failure
Definition: effects of the failure mode on the function as perceived by the customer
Ask yourself- ”What would be the result of this failure?” or “If the failure occurs then what are the consequences”
Describe the effects in terms of what the customer might experience or notice
State clearly if the function could impact safety or noncompliance to regulations
Identify all potential customers. The customer may be an internal customer, a distributor as well as an end user
Describe in terms of product performance

## Slide 37
Effect(s) of Failure
EXAMPLE:
Cannot see out of front window
Air conditioner makes cab too cold
Does not get warm enough
Takes too long to heat up
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 38
Examples of Potential Effects
Noise
loss of fluid
seizure of adjacent surfaces
loss of function
no/low output
loss of system
Intermittent operations
rough surface
unpleasant odor
poor appearance
potential safety hazard
Customer dissatisfied

## Slide 39
Severity
Definition: assessment of the seriousness of the effect(s) of the potential failure mode on the next component, subsystem, or customer if it occurs
Severity applies to effects
For failure modes with multiple effects, rate each effect and select the highest rating as severity for failure mode

## Slide 40
Severity
EXAMPLE:
Cannot see out of front window – severity 9
Air conditioner makes cab too cold – severity 5
Does not get warm enough – severity 5
Takes too long to heat up – severity 4
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 41
Classification
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function
Classification should be used to define potential critical and significant characteristics
Critical characteristics (9 or 10 in severity with 2 or more in occurrence-suggested) must have associated recommended actions
Significant characteristics (4 thru 8 in severity with 4 or more in occurrence -suggested) should have associated recommended actions
Classification should have defined criteria for application
EXAMPLE:
Cannot see out of front window – severity 9 – incorrect vent location – occurrence 2
Air conditioner makes cab too cold – severity 5 - Incorrect routing of vent hoses (too close to heat source) – occurrence 6

## Slide 42
Potential Cause(s)/Mechanism(s) of failure
Definition: an indication of a design weakness, the consequence of which is the failure mode
Every conceivable failure cause or mechanism should be listed
Each cause or mechanism should be listed as concisely and completely as possible so efforts can be aimed at pertinent causes

## Slide 43
Cause(s) of Failure
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
Potential
Effect(s) of
Failure
Function
EXAMPLE:
Incorrect location of vents
Incorrect routing of vent hoses (too close to heat source)
Inadequate coolant capacity for application

## Slide 44
Potential Cause Mechanism
Tolerance build up
insufficient material
insufficient lubrication capacity
Vibration
Foreign Material
Interference
Incorrect Material thickness specified
exposed location
temperature expansion
inadequate diameter
Inadequate maintenance instruction
Over-stressing
Over-load
Imbalance
Inadequate tolerance
Yield
Fatigue
Material instability
Creep
Wear
Corrosion

## Slide 45
Occurrence
Definition: likelihood that a specific cause/mechanism will occur
Be consistent when assigning occurrence
Removing or controlling the cause/mechanism though a design change is only way to reduce the occurrence rating

## Slide 46
Occurrence
EXAMPLE:
Incorrect location of vents – occurrence 3
Incorrect routing of vent hoses (too close to heat source) – occurrence 6
Inadequate coolant capacity for application – occurrence 2
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 47
Current Design Controls
Definition: activities which will assure the design adequacy for the failure cause/mechanism under consideration
Confidence Current Design Controls will detect cause and subsequent failure mode prior to production, and/or will prevent the cause from occurring
  If there are more than one control, rate each and select the lowest for the detection rating
Control must be allocated in the plan to be listed, otherwise it’s a recommended action
3 types of Controls
  1. Prevention from occurring or reduction of rate
  2. Detect cause mechanism and lead to corrective actions
  3. Detect the failure mode, leading to corrective actions

## Slide 48
Current Design Controls
EXAMPLE:
Engineering specifications (P) – preventive control
Historical data (P) – preventive control
Functional testing (D) – detective control
General vehicle durability (D) – detective control
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 49
Examples of Controls
Type 1 control
  Warnings which alert product user to impending failure
  Fail/safe features
  Design procedures/guidelines/ specifications
Type 2 and 3 controls
  Road test
  Design Review
  Environmental test
  fleet test
  lab test
  field test
  life cycle test
  load test

## Slide 50
Detection
Detection values should correspond with AIAG, SAE
If detection values are based upon internally defined criteria, a reference must be included in FMEA to rating table with explanation for use
Detection is the value assigned to each of the detective controls
Detection values of 1 must eliminate the potential for failures due to design deficiency
EXAMPLE:
Engineering specifications – no detection value
Historical data – no detection value
Functional testing – detection 3
General vehicle durability – detection 5
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 51
RPN (Risk Priority Number)
Risk Priority Number is a multiplication of the severity, occurrence and detection ratings
Lowest detection rating is used to determine RPN
RPN threshold should not be used as the primary trigger for definition of recommended actions
EXAMPLE:
Cannot see out of front window – severity 9, – incorrect vent location – 2, Functional testing – detection 3, RPN - 54
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 52
Risk Priority Number(RPN)
Severity x Occurrence x Detection
RPN is used to prioritize concerns/actions
The greater the value of the RPN the greater the concern
RPN ranges from 1-1000
The team must make efforts to reduce higher RPNs through corrective action
General guideline is over 100 = recommended action

## Slide 53
Risk Priority Numbers (RPN's)
Severity
  Rates the severity of the potential effect of the failure.
Occurrence
  Rates the likelihood that the failure will occur.
Detection
  Rates the likelihood that the problem will be detected before it reaches the end-user/customer.
RPN rating scales usually range from 1 to 5 or from 1 to 10, with the higher number representing the higher seriousness or risk.

## Slide 54
RPN Considerations
Rating scale example:
  Severity = 10 indicates that the effect is very serious and is “worse” than Severity = 1.
  Occurrence = 10 indicates that the likelihood of occurrence is very high and is “worse” than Occurrence = 1.
  Detection = 10 indicates that the failure is not likely to be detected before it reaches the end user and is “worse” than Detection = 1.
1 5 10

## Slide 55
RPN Considerations (continued)
RPN ratings are relative to a particular analysis.
  An RPN in one analysis is comparable to other RPNs in the same analysis …
  … but an RPN may NOT be comparable to RPNs in another analysis.
1 5 10

## Slide 56
Because similar RPN's can result in several different ways (and represent different types of risk), analysts often look at the ratings in other ways, such as:
  Occurrence/Severity Matrix (Severity and Occurrence).
  Individual ratings and various ranking tables.
1 5 10
RPN Considerations (continued)

## Slide 57
Recommended Actions
Definition: tasks recommended for the purpose of reducing any or all of the rankings
Only design revision can bring about a reduction in the severity ranking
Examples of Recommended actions
  Perform:
    Designed experiments
    reliability testing
    finite element analysis
  Revise design
  Revise test plan
  Revise material specification

## Slide 58
Recommended Actions
All critical or significant characteristics must have recommended actions associated with them
Recommended actions should be focused on design, and directed toward mitigating the cause of failure, or eliminating the failure mode
If recommended actions cannot mitigate or eliminate the potential for failure, recommended actions must force characteristics to be forwarded to process FMEA for process mitigation
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 59
Responsibility & Target Completion Date
All recommended actions must have a person assigned responsibility for completion of the action
Responsibility should be a name, not a title
Person listed as responsible for an action must also be listed as a team member
There must be a completion date accompanying each recommended action
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 60
Action Results
Unless the failure mode has been eliminated, severity should not change
Occurrence may or may not be lowered based upon the results of actions
Detection may or may not be lowered based upon the results of actions
If severity, occurrence or detection ratings are not improved, additional recommended actions must to be defined
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Target
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Design
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Potential
Failure
Mode
Item
Detect
Prevent
R
P
N
D
E
T
O
C
C
S
E
V
Action
Taken
Action Results
Response &
Complete
Date
Recommended
Actions
R
P
N
D
e
t
e
c
Current
Controls
O
c
c
u
r
Potential
Cause(s)/
Mechanism(s)
Of Failure
C
l
a
s
s
S
e
v
Potential
Effect(s) of
Failure
Function

## Slide 61
Exercise Design FMEA
Perform A DFMEA on a pressure cooker

## Slide 63
Pressure Cooker Safety Features
1. Safety valve relieves pressure before it reaches dangerous levels.
2. Thermostat opens circuit through heating coil when the temperature rises above 250° C.
3. Pressure gage is divided into green and red sections. "Danger" is indicated when the pointer is in the red section.

## Slide 64
Pressure Cooker FMEA
Define Scope:
1. Resolution - The analysis will be restricted to the four major subsystems (electrical system, safety valve, thermostat, and pressure gage).
2. Focus - Safety

## Slide 65
Pressure cooker block diagram

## Slide 66
Process FMEA
Definition:
  A documented analysis which begins with a teams thoughts concerning requirements that could go wrong and ending with defined actions which should be implemented to help prevent and/or detect problems and their causes.
  A proactive tool to identify concerns with the sources of variation and then define and take corrective action.

## Slide 67
PFMEA as a tool…
To access risk or the likelihood of significant problem
Trouble shoot problems
Guide improvement aid in determining where to spend time and money
Capture learning to retain and share knowledge and experience

## Slide 68
Process
Flow
Diagram
Process FMEA
Process
Control
Plan
Operator
Job
Instructions
Conforming Product
Reduced Variation
Customer Satisfaction
Customer Requirements
Deign Specifications
Key Product Characteristics
Machine Process Capability

## Slide 69
Inputs for PMEA
Process flow diagram
Assembly instructions
Design FMEA
Current engineering drawings and specifications
Data from similar processes
  Scrap
  Rework
  Downtime
  Warranty

## Slide 70
Process Function Requirement
Brief description of the manufacturing process or operation
The PFMEA should follow the actual work process or sequence, same as the process flow diagram
Begin with a verb

## Slide 71
Team Members for a PFMEA
Process engineer
Manufacturing supervisor
Operators
Quality
Safety
Product engineer
Customers
Suppliers

## Slide 72
PFMEA Assumptions
The design is valid
All incoming product is to design specifications
Failures can but will not necessarily occur
Design failures are not covered in a PFMEA, they should have been part of the design FMEA

## Slide 73
Potentional Failure Mode
How the process or product may fail to meet design or quality requirements
Many process steps or operations will have multiple failure modes
Think about what has gone wrong from past experience and what could go wrong

## Slide 74
Common Failure Modes
Assembly
  Missing parts
  Damaged
  Orientation
  Contamination
  Off location
Torque
  Loose or over torque
  Missing fastener
  Cross threaded
Machining
  Too narrow
  Too deep
  Angle incorrect
  Finish not to specification
  Flash or not cleaned

## Slide 75
Potentional failure modes
Sealant
  Missing
  Wrong material applied
  Insufficient or excessive material
  dry
Drilling holes
  Missing
  Location
  Deep or shallow
  Over/under size
  Concentricity
  angle

## Slide 76
Potential effects
Think of what the customer will experience
  End customer
  Next user-consequences due to failure mode
May have several effects but list them in same cell
The worst case impact should be documented and rated in severity of effect

## Slide 77
Potential Effects
End user
  Noise
  Leakage
  Odor
  Poor appearance
  Endangers safety
  Loss of a primary function
  performance
Next operation
  Cannot assemble
  Cannot tap or bore
  Cannot connect
  Cannot fasten
  Damages equipment
  Does not fit
  Does not match
  Endangers operator

## Slide 78
Severity Ranking
How the effects of a potential failure mode may impact the customer
Only applies to the effect and is assigned with regard to any other rating
Potential effects of failure | Severity
Cannot assemble bolt(5) Endangers operator(10) Vibration (6) | 10 Take the highest effect ranking

## Slide 79
Classification
Use this column to identify any requirement that may require additional process control
  ∙KC∙ - key characteristic
  ∙F∙ – fit or function
  ∙S∙ - safety
  Your company may have a different symbol

## Slide 80
Potential Causes
Cause indicates all the things that may be responsible for a failure mode.
Causes should items that can have action completed at the root cause level (controllable in the process)
Every failure mode may have multiple causes which creates a new row on the FMEA
Avoid using operator dependent statements i.e. “operator error” use the specific error such as “operator incorrectly located part” or “operator cross threaded part”

## Slide 81
Potential Causes
Equipment
  Tool wear
  Inadequate pressure
  Worn locator
  Broken tool
  Gauging out of calibration
  Inadequate fluid levels
Operator
  Improper torque
  Selected wrong part
  Incorrect tooling
  Incorrect feed or speed rate
  Mishandling
  Assembled upside down
  Assembled backwards

## Slide 82
Occurrence Ranking
How frequent the cause is likely to occur
Use other data available
  Past assembly processes
  SPC
  Warranty
Each cause should be ranked according to the guideline

## Slide 83
Current Process Controls
All controls should be listed, but ranking should occur on detection controls only
List the controls chronologically
  Don not include controls that are outside of your plant
Document both types of process controls
  Preventative- before the part is made
    Prevent the cause, use error proofing at the source
  Detection- after the part is made
    Detect the cause (mistake proof)
    Detect the failure mode by inspection

## Slide 84
Process Controls
Preventative
  SPC
  Inspection verification
  Work instructions
  Maintenance
  Error proof by design
  Method sheets
  Set up verification
  Operator training
Detection
  Functional test
  Visual inspection
  Touch for quality
  Gauging
  Final test

## Slide 85
Detection
Probability the defect will be detected by process controls before next or subsequent process, or before the part or component leaves the manufacturing or assembly location
Likely hood the defect will escape the manufacturing location
Each control receives its own detection ranking, use the lowest rating for detection

## Slide 86
Risk Priority Number (RPN)
RPN provides a method for a prioritizing process concerns
High RPN’s warrant corrective actions
Despite of RPN, special consideration should be given when severity is high especially in regards to safety

## Slide 87
RPN as a measure of risk
An RPN is like a medical diagnostic, predicting the health of the patient
At times a persons temperature, blood pressure, or an EKG can indicate potential concerns which could have severe impacts or implications

## Slide 88
Control
Influence
Can’t control or influence at this time
Recommended actions

## Slide 89
Recommended Action
Definition: tasks recommended for the purpose of reducing any or all of the rankings
Examples of Recommended actions
  Perform:
    Process instructions (P)
    Training (P)
    Can’t assemble at next station (D)
    Visual Inspection (D)
    Torque Audit (D)

## Slide 90
Process
Control
Plan
Operator
Job
Instructions
Process
Flow
Diagram
Process
Changes
Current or
Expected
quality
performance
Customer
Design
requirements
Implementation
and verification
Recommended
Corrective actions
i.e.
Error proofing
Continuous Improvement Efforts
And RPN reduction loop
Communication of standard
of work to operators
PMEA as a Info Hub
Process FMEA document

## Slide 92
Process FMEA exercise
Task: Produce and mail sets of contribution requests for Breast Cancer research
Outcome: Professional looking requests to support research for a cure, 50 sets of information, contribution request, and return envelope

## Slide 93
Requirements
No injury to operators or users
Finished dimension fits into envelope
All items present (info sheet, contribution form, and return envelope) {KEY}
All pages in proper order (info sheet, contribution form, return envelope) {KEY}
No tattered edges
No dog eared sheets
Items put together in order (info sheet [folded to fit in legal envelope], contribution sheet, return envelope) {KEY}
General overall neat and professional appearance
Proper first class postage on envelopes
Breast cancer seal on every envelope sealing the envelope on the back
Mailing label, stamp and seal on placed squarely on envelope {KEY}
Rubber band sets of 25

## Slide 94
Process steps
Fold information sheet to fit in legal envelope
Collate so each group includes all components
Stuff envelopes
Affix address, postage, and seal
Rubber bands sets of 25
Deliver to post office for mail today by 5 pm

## Slide 95
My hints for a successful FMEA
Take your time in defining functions
Ask a lot of questions:
  Can this happen…..
  What would happen if the user….
Make sure everyone is clear on Function
Be careful when modifying other FMEAs

## Slide 96
10 steps to conduct a FMEA
Review the design or process
Brainstorm potential failure modes
List potential failure effects
Assign Severity ratings
Assign Occurrence ratings
Assign detection rating
Calculate RPN
Develop an action plan to address high RPN’s
Take action
Reevaluate the RPN after the actions are completed

## Slide 97
Reasons FMEA’s fail
One person is assigned to complete the FMEA.
Not customizing the rating scales with company specific data, so they are meaningful to your company
The design or process expert is not included in the FMEA or is allowed to dominate the FMEA team
Members of the FMEA team are not trained in the use of FMEA, and become frustrated with the process
FMEA team becomes bogged down with minute details of design or process, losing sight of the overall objective

## Slide 98
Reasons FMEA’s fail
6. Rushing through identifying the failure modes to move onto the next step of the FMEA
7. Listing the same potential effect for every failure i.e. customer dissatisfied.
8. Stopping the FMEA process when the RPN’s are calculated and not continuing with the recommended actions.
9. Not reevaluating the high RPN’s after the corrective actions have been completed.

## Slide 99
Software Recommendations
Numerous types and specialized formats
Many have free trials
  X-FMEA Reliasoft
  FMEA Pro-7
  Access Data bases
  Excel formats

## Slide 100
FMEA Jeopardy
Potpourri
Methods
Rankings
SOD
$200
$300
$400
$500
$100
$200
$300
$400
$500
$100
$200
$300
$400
$500
$100
$200
$300
$400
$500
$100
Sample

## Slide 101
Bibliography
MIL-STD-1629A , Procedures for Performing a Failure Mode, Effects and Criticality Analysis, Nov. 1980.
Sittsamer, Risk Based Error-Proofing, The Luminous Group, 2000
MIL-STD-882B, 1984.
O’Conner, Practical Reliability Engineering, 3rd edition, Revised, John Wiley & Sons,Chichester, England, 1996.
QS9000 FMEA reference manual (SAE J 1739)
McDerrmot, Mikulak, and Beauregard, The Basics of FMEA, Productivity Inc., 1996.