## Slide 1
Fluid Power Defined

## Slide 2
Definitions
Pascal's law states that when there is an increase in pressure at any point in a confined fluid, there is an equal increase at every other point in the container.
Force= Pressure x Area
Pressure= Force
Area
Area= Force
Pressure
F
P
A
Notes: http://www.grc.nasa.gov/WWW/k-12/WindTunnel/Activities/Pascals_principle.html

## Slide 3
Basic Terms

## Slide 4
Notes
1 N/m2 is also called a Pascal denoted by Pa.
  1 PSI = 6895 Pa.
  1 N/mm2 is also called a Mega Pascal denoted by MPa.
  1 PSI = .006895 MPa.
  BAR (Average Barometric Pressure) 14.5 PSI = 105 Pa.

## Slide 5
Definitions
5 LBS
FORCE
PISTON A =1/2 SQ INCH AREA
100 LBS
FORCE
PISTON B =10 SQ INCH AREA
The word “hydraulics” generally refers to power produced by moving liquids.

## Slide 6
Definitions
The word “hydraulics” generally refers to power produced by moving liquids.
22.2 NEWTONS
PISTON A =1/2 SQ INCH AREA
444.8 NEWTONS
PISTON B =10 SQ INCH AREA

## Slide 7
Fluid - can be almost any liquid. The most common hydraulic fluids contain specially compounded petroleum oils that lubricate and protect the system from corrosion.
Reservoir - acts as a storehouse for the fluid and a heat dissipater.
Hydraulic pump - converts the mechanical energy into hydraulic energy by forcing hydraulic fluid, under pressure, from the reservoir into the system.
Definitions
Hydraulic systems contain the following key components:

## Slide 8
Fluid lines - transport the fluid to and from the pump through the hydraulic system. These lines can be rigid metal tubes, or flexible hose assemblies. Fluid lines can transport fluid under pressure or vacuum (suction).
Hydraulic valves - control pressure, direction and flow rate of the hydraulic fluid.
Actuator - converts hydraulic energy into mechanical energy to do work. Actuators usually take the form of hydraulic cylinders. Hydraulic cylinders are used on agricultural, construction, and industrial equipment.
Definitions
Notes: NOTE: when compromised, industrial hydraulic lines can present danger to operators. Fluid is under extreme pressure and can act as a “water jet” and cut or pierce anything around the leak.

## Slide 9
Case Study-Calatrava Pavillion

## Slide 10
The 72 fins of varying lengths weigh 100 tons and are moved with hydraulic cylinders in a slow curling grace.
Case Study-Calatrava Pavillion

## Slide 11
Case Study-Calatrava Pavillion

## Slide 12
Maintenance Crew with Replacement Cylinder
Case Study-Calatrava Pavillion

## Slide 13
A project of epic proportions. Nelson Bros. use a crane to hoist the cylinders into place
Case Study-Calatrava Pavillion
Notes: 2012 Nelson Bros. & Strom went to work on modifying the hydraulic control blocks (cylinders) so they would safely alleviate excess the pressure within the hydraulic circuit. These cylinders pump the hydraulic fluid that allow the Calatrava to open and close its wings.