## Slide 1
Heat Loss and Efficiency
The Janitor’s Dilemma

## Slide 2
Gulf Course Case Study
Many older schools made of concrete and glass due to low material costs
  Are they cost effective in the long run?
At what temperature will the janitor turn the heat on to keep the temperature at 68 with 30 students in the room?

## Slide 3
Part A
One BTU or British Thermal Unit is an English standard unit of energy
  One BTU is the amount of thermal energy required to raise the temperature of one pound of pure liquid water by one degree Fahrenheit at which water has its greatest density (39F)
    Equivalent to approximately 1055 joule
      1055 watt-seconds

## Slide 4
Part A
One WATT is equal to 3.413 BTU/Hour
One average person is equal to 108.000 watts
One average person gives off heat equal to 368.694 BTU/Hour
R-Value (R) is the resistance level of a material to temperature change
  Determined by building materials list or derived from an experiment done to find R-Value
U-Factor is the combined thermal conductivity (1/R)
Delta T (rT) is the change in temperature
  Outside temp is -20F and inside is 70F
    rT is 90F

## Slide 5
Part B
Calculate the area of materials being used.
The answers should be in feet and converted to the nearest thousandth of a decimal
The R-Value of the glass used is .890
The R-Value of concrete is 1.110 per 8”
The ceilings R-Value is .080 per inch thickness
West Wall
  West Wall Total (AW)
  West Wall Glass(AWG)
  West Wall Concrete (AWC)
North Wall
  North Wall Total (AN)
  North Wall Glass(ANG)
  North Wall Concrete (ANC)
Ceiling
  Ceiling Total (AC)

## Slide 6
12’4”
30’0”
Concrete
Glass
Glass
Glass
Glass
Glass
2’0”
7’3”
West Wall
RValue-Glass = .890
RValue-Concrete = 1.110

## Slide 7
North Wall
RValue-Glass = .890
RValue-Concrete = 1.110
12’4”
30’0”
Concrete
Glass
12’0”
7’3”

## Slide 8
Ceiling
RValue per 1” = .080
Ceiling Thickness = 5”
30’0”
30’0”
Concrete

## Slide 9
Part C
Calculate R-Values for wall sections.
These are proportional calculations
  Multiple layers are totaled together

## Slide 10
Part C
West Wall
  Rw = (AWG)(RValue-Glass)+(AWC)(RValue-Concrete)
North Wall
  RN = (ANG)(RValue-Glass)+(ANC)(RValue-Concrete)
Ceiling
  RC = (AC)(5” thick)(RValue per 1”)

## Slide 11
Part C
Calculate Overall R-Value
  RValue = (RW+RN+RC) / (AW+AN+AC)
Calculate U-Factor
  U Factor = 1 / (RValue)
Calculate Heat Loss
  (Surface Area)(U Factor)(rT) = Heat loss in BTU’s / Hour
  Plug in variables you know and solve for not known

## Slide 12
Question and Grading
Questions
  What temperature outside does it have to be when the students own body heat will not keep the room at 68F?
  Why?