## Slide 1
Using the Multimeter

## Slide 2
What is a Multimeter?
A multimeter is a tool used to measure electricity in a circuit. It can measure:
Voltage (V) – how strong the electrical push is
Current (A) – how much electricity is flowing
Resistance (Ω) – how much a material resists electricity

## Slide 3
Parts of a Multimeter
A basic multimeter has three main parts:
Display Screen – shows the measurement
Dial / Selector – chooses what to measure

## Slide 4
Parts of a Multimeter
Test Leads (Probes)
  Red probe → Positive (+)
  Black probe → Negative (–)

## Slide 5
Understanding the Dial
V (Voltage) – electrical pressure
A (Current) – flow of electricity
Ω (Resistance) – opposition to flow
))) (Continuity)– checks if a path is complete

## Slide 6
Safety Rules
Never touch bare metal tips of the probes
Keep hands dry
Do not force the probes into components
Always follow the instructions carefully
Ask for help if unsure

## Slide 7
Measuring Voltage
Voltage tells us how much energy electricity has. To measure voltage:
Turn the dial to V 20V
Place the black probe on the negative (–)
Place the red probe on the positive (+)
Read the number on the screen

## Slide 8
Measuring Battery Voltage
When testing a battery:
Red probe → battery positive (+)
Black probe → battery negative (–)
If the number is:
Close to the battery label → battery is good
Much lower → battery is weak or dead

## Slide 9
What is Continuity?
Continuity checks if electricity can:
Travel through a wire or component
Complete a full path (closed circuit)
If electricity can flow → circuit is complete
If not → circuit is broken

## Slide 10
Checking Continuity
Turn the dial to the continuity symbol
Touch probes to both ends of a wire or component
Listen for a beep
  Beep sound → electricity can flow
  No sound → broken connection