## Slide 1: Fundamentals of Lab Work
Objective D: Identify the Proper Way to Use Different Lab Tools

## Slide 2
Selecting a Tool for the Job
Many times a product can be made using many different machines
What are some things that might affect what machine we choose to use?
  Is the machine specified in the Technical Drawings?
  Is this a safe operation to do using a tool?
  Can the machine manipulate the material being used?
  Is the tool the most efficient for the operation?
  Is the tool safe to operate?
  Is anyone certified to use the tool?

## Slide 3
Material Qualities
The qualities of a material will affect how well a tool can perform a function
Some tools require special bits or blades to work on different materials
Some tools may only be used on one material
The material may determine which tool is best used to complete the operation
Qualities
Brittleness
  having hardness and rigidity but little tensile strength; breaking readily with a comparatively smooth fracture, as glass.
Ductility
  able to undergo change of form without breaking. capable of being molded or shaped; plastic.
Hardness
  the measured resistance of a metal to indention, abrasion, deformation, or machining.
All qualities definitions on this page from www.dictionary.com

## Slide 4
Activity Time!
Identify which qualities each of the following materials exhibit
Material | Brittleness | Ductility | Hardness
Sheet Steel |  |  | 
Wood |  |  | 
Glass |  |  | 
Acrylic |  |  | 
Copper Pipe |  |  | 
Fiberglass |  |  | 
Styrofoam |  |  | 
Steel Rod |  |  | 

## Slide 5
Tool Selection
Softer Materials are easier to cut and create less friction
Smaller areas to be machined have less surface area, therefore less friction
  Faster Feed Speed
  Faster Tool Speed
  Less cutting surfaces (less teeth or flutes)
  Can take aggressive or deeper cuts
Harder Materials create more friction with the cutting tool
Larger areas to be machined means increased surface area contact with the tool= more friction
  Slower Feed Speed
  Slower Tool Speed
  Increase the amount cutting surfaces
  Take shallower cutting passes

## Slide 6
Common Machine Components
Primary Power
  Power coming into the machine
  Can the machine be unplugged or is it hard wired
  How many ways can power be disconnected from the machine?
Machine Power Switch
  Is there a switch or a trigger mechanism?
Tooling Holders
  How is the tool held to the machine?
    Collet
    Chuck
    Arbor
Guards
  Shield Operator from tooling & Debris
Table or Base
  Is machine Portable or Stationary?
  How is machine mounted to table or base?
  Tooling should be used such that the material is allowed to rest on the base or table
Jigs & Fixtures
  Devices used to allow repetitive operations
  Are there jigs & fixtures that can be used on more than one machine?

## Slide 7
Stationary Power Tools
Drill Press
  For Drilling Operations
Band Saw
  For cutting curves and small parts
Bench Grinder
  For rounding edges and sharpening
Compound Miter Saw
  For fast cutting of wood stock
  Can cut accurate angles
Welder
  For joining similar metals
Metal Chop Saw
  For fast cutting of steel stock
  Can cut accurate angles

## Slide 8
Portable Power Tools
Jig Saw
  For cutting curves and internal features
Circular Saw
  For fast, straight cuts on wood
Sanders
  For smoothing and removing surface contaminants
Propane Torch
  For heating materials
Angle Grinder
  For removing material
Drill
  For cutting holes or driving screws
Router
  For cutting operations on wood or plastic

## Slide 9
Non- Power Tools
Bench Vise
  For holding work piece stationary
C-Clamps
  For holding work to a table or base
Adjustable Bar Clamps
  For holding work or applying pressure
Locking Pliers
  For holding work pieces together
Pipe Cutter
  For cutting pipe
Glass Cutter
  For cutting glass without cracking
Files
  For removal of material
Chisels
  For removal of material
Rivet Gun
  For the installation of Rivets
Hammer
  For applying force
Hacksaw
  For the cutting of hard materials
Socket Wrench
  For manipulating fasteners
Wrench
  For manipulating fasteners
Screwdriver
  For manipulating fasteners
Spray Paint Can
  For application of finish materials
Can you think of more?

## Slide 10
Operating Machines
Safety Apparel
  Safety Glasses must be worn at all times in lab!
  Hair or clothing that can get caught in tooling must be restrained
Body Position
  Relaxed stance that provides support
  Position body in such a way that material can be supported and machine operated comfortably
Material Positioning
  Material should rest on stable surface
  Use an assistant to help if necessary
Safety Zone
  Only the operator should be in the safety zone

## Slide 11
Activity Time!
Follow the Instructor into the lab and observe the operating procedures for the machines