## Slide 1: Fundamentals of Lab Work
Objective F: Understand How to Develop a Plan for Procedure for Manufacturing a Product

## Slide 2
Using the technical drawings or documents, we need to identify:
  Sizes of Product
  Materials to be used
  Processes for machining parts
  Processes for assembly
This may require communication with designer/engineer
Information Needed from Technical Drawing

## Slide 3
A Cut List tells the laborer what sizes the materials need to be cut to
  Allows a skilled laborer to prepare jobs for less skilled laborers
  Streamlines the process by getting all the parts ready
  Allows for materials to more efficiently be used
How to make a cut list:
  Identify the parts needed to create product
  Separate parts by materials
  Identify the size of each part
  Create a list by material, listing sizes and part names
  Show quantity of parts
  List total amount of material needed
Creating a Cut List​

## Slide 4
Example Cut List
¾” Plywood
  (2) 6” x 12” Side Pieces (1 sq. ft)
  (1) 6” x 6” Back Piece (.25 sq. ft)
  (2) 9” x 14” Roof Pieces (1.75 sq. ft)
  (1) 6” x 12” Bottom Piece (.5 sq. ft)
½” Dowel Rod
  (1) 6” Feeder Perch (6 ln. in)
1/8” Acrylic Sheet
  (1) 6” x 6” Front (.25 sq ft)

## Slide 5
Creating a plan for the Manufacturing Process
  Identifies how materials will be machined
  Identifies order that parts will be created
  Lists what equipment should be used for each process
  Identifies fastening methods to be used
  Can help to determine which processes will be completed by different laborers
Plan For Procedure

## Slide 6
Use tablesaw to cut one (1) 6” Strip from the ¾” Plywood sheet
Use Compound Miter Saw to cut three (3) 12” Sections of the 6” Strips (Bottom & Side Pieces)
Use Compound Miter Saw to cut one (1) 6” Section of the 6” Strips (Back)
Set tablesaw angle to 45 degrees. Cut one 9” Wide Strip from the ¾” Plywood sheet
Use Compound Miter Saw to cut two (2) 14” Sections from the 9” Strip with 45 degree edges (Roof Pieces)
Use Compound Miter Saw to cut one (1) 6” section from the ½” Dowel Rod (Feeder Perch)
Mark out a 6” by 6” square on the sheet of 1/8” Acrylic
Use Masking tape to layout the 6” x 6” square and cut one (1) using the tablesaw (Front Piece)
Remove the masking tape that is left on the front piece
Using the drill press, 7/64” drill bit and side piece jig to bore pilot holes in (2) side pieces
Align the bottom piece, back piece and front piece to the left side piece
Use the cordless drill to drive the #8 x 1-1/4” screws to attach the back, front and bottom pieces to the left side piece
Flip over assembled side and align the right side piece
Use the cordless drill to drive the #8 x 1-1/4” screws to attach the back, front and bottom pieces to the right side piece
Apply glue to 45 degree edge of one (1) roof piece
Align the two 45 degree edges of the roof pieces together and brad nail them together
Using brad nailer, attach the roof to the top of the side pieces.
Example Plan for Procedure

## Slide 7
Create a Cut List and a Plan for Procedure for making the Tool Box Show in the drawing to the right
Activity Time!